## Slide 1
Well Permit Testing Update - May 2024

## Slide 2: Approach to comply with Executive Order
Use Butte Valley as example
Evaluate depth and capacity of wells and run model scenarios looking at hypothetical new wells with a combination of depth and capacity
Evaluate drawdown at the well and radius of influence
Next steps:
  Develop a well inventory to include consideration of possible impact to nearby wells
  For each zone withing the Butte valley basin, develop tables with criteria to provide preliminary guidelines
  Same approach can be then implemented in Scott and Shasta

## Slide 3: DWR Well Completion Report dataset
Not all wells provide reports
Not all drillers pump test data
Pumping rates may be wrong
The best available data for an initial study
  Only considering non-exempt wells under the Executive Order
  Only considering wells since 1989 to gain an understanding of recent conditions

## Slide 4: Total Depth of non-exempt wells in Butte
Total Completed Depth dataset is complete. All wells provide depth data
The average depth is 448 feet
The median depth is 400 feet (half are deeper and half are shallower)

## Slide 5: Well Yield of non-exempt wells in Butte
37 out of 43 non-exempt wells provided pump test data from 1989-2024
The average yield is 1355 gpm
The median yield is 1387 gpm (half are less and half are more)

## Slide 6: 138 hypothetical wells
23 combinations of well construction
6 preliminary locations in and around Butte Valley
PUMPING SCENARIOS:
A variety of pumping scenarios considered (depth, rate):
  Depth: 200, 400, 600, 800, 1200 ft
  Capacity: 600, 800, 1200, 1600, 2000, 2500, and 3000 gpm
Predictions were made by placing a hypothetical well within the Butte Valley Basin
Observing drawdown as predicted by the model

## Slide 7: Approximate Well Locations
Approximate locations of non-domestic well in the Butte Valley area.
Circled area are where hypothetical pump tests are being calculated
The Executive Order allows setting limits on wells both inside and outside the SGMA basin

## Slide 8: Limitations
The model has generally good correlation between observed and predicted groundwater levels
Does not bias significantly to over or under prediction
  Not over or under estimating
Still needs further calibration

## Slide 9: ZONE 1: North Well
Pumping starts in April
Results are presented for August

## Slide 10
Well Depth: 800 ft Pumping rate: 3000 gpm
August 2023
Drawdown at Well Cell: 123.8 ft, larger impact
Well Depth: 1200 ft Pumping rate: 1200 gpm
Drawdown at Well Cell: 54.3 ft, takes longer to decline
August 2023
August 2023
Well Depth: 600 ft Pumping rate: 600 gpm
Drawdown at Well Cell: 22.2 ft., rapidly declining to 2 ft within approximately 1 mile

## Slide 11: ZONE 2: Central Well
Pumping starts in April
Results are presented for August

## Slide 12
Well Depth: 800 ft Pumping rate: 3000 gpm
August 2023
August 2023
Well Depth: 1200 Pumping rate: 1200 gpm
Well Depth: 600 ft Pumping rate: 600 gpm
August 2023
Drawdown at Well Cell: 130 ft.
Drawdown at Well Cell: 54.5 ft.
Drawdown at Well Cell: 24 ft.

## Slide 13: Summary and next steps
Once all the scenarios are finalized: what is the accepted drawdown? Are there other wells nearby?
For each zone, develop summary table:
ZONE | Depth (ft) | Capacity (gpm) | Expected drawdown (ft) | Expected radius of influence (ft) | Are there other wells nearby? | Can it be permitted or needs more analysis?
1 | 800 | 3000 | 10 | 1000 | Yes | Needs more analysis

## Slide 14
Thank You